## Slide 1: Electronic System Components

## Slide 4: Signal Modification and Conditioning
Signal modification includes signal conversion and signal conditioning and processing.
It plays a crucial role in component interconnection or interfacing. The reasons for this include the following:
When two components are interconnected, their signals are altered (due to dynamic coupling/interaction).
For matching of the interconnected components, their operating signals may have to be modified(with regard to power, type, etc.).
For the purpose of the application, the signal type and characteristics may have to be modified(e.g., power, analog–digital conversion, modulation).
In view of noise and other errors, and system requirements, the signals
have to be conditioned(e.g., filtering, amplification
25

## Slide 5: Why Signal Conditioning
26

## Slide 6: Signal-Modification Hardware
Voltage Follower : Figure shows an op amp circuit with unity gain and very high input impedance. The input impedance is essentially the input impedance of the op amp itself, which can be greater than 100 MOhm .
The op amp voltage follower.
This but
circuit has unity gain very high input
impedance.

## Slide 7: Signal-Modification Hardware
The unity gain voltage follower impedance transformer in the sense
of converting
is essentially an
a
voltage at high impedance to the same voltage at low impedance.
Inverting Amplifier: Equation shows that this circuit inverts the input signal and may have either attenuation or gain, depending on the ratio of input resistance,R1 , and feedback resistance,R2 .

## Slide 8: Signal-Modification Hardware
Summing Amplifier A common modification of the
  inverting amplifier is an amplifier that sums or adds two or
  more applied voltages.
  This circuit is shown in Figure for the case of summing two i voltages. The transfer function of this amplifier is given by

## Slide 9: Signal-Modification Hardware
Example : Develop an op amp circuit that can provide an output voltage related to the input voltage by

## Slide 10: Signal-Modification Hardware
Non inverting Amplifier :A non inverting amplifier may be constructed from an op amp, as shown in Figure . The gain of this circuit is found by summing the currents at the summing point, S, and using the fact that the summing point voltage is Vin so that no voltage difference appears across the input terminals.

## Slide 11: Signal-Modification Hardware
Instrumentation
Differential
differential amplifier
provides an output
Amplifier: An
voltage
ideal with
respect to ground that is some gain times the difference between two input voltages
where A is the differential gain and both Va and Vb are voltages with respect to ground. Such an amplifier plays an important role in instrumentation and measurement.

## Slide 12: Signal-Modification Hardware
Differential Amplifier There are a number of op amp circuits for differential amplifiers. The most common circuit for this amplifier is shown in Figure

## Slide 13: Signal-Modification Hardware
Instrumentation Amplifier Differential
amplifiers
with
high input impedance and low output impedance are given the special name of instrumentation amplifier. They find a host of applications in process-measurement systems, principally as the initial stage of amplification for bridge circuits.
Example: A sensor outputs a range of 20.0 to 250 mV as a variable varies over its range. Develop signal conditioning so that this becomes 0 to 5 V. The circuit must have very high input impedance.

## Slide 14: OPAMP CIRCUITS IN INSTRUMENTATION
Voltage-to-Current Converter: Because signals in process control are most often transmitted as a current, specifically 4 to 20 mA, it is often necessary to employ a linear voltage-to-current converter. Such a circuit must be capable of sinking a current into a number of different loads without changing the voltage-to-current transfer characteristics.

## Slide 15: OPAMP CIRCUITS IN INSTRUMENTATION

## Slide 16: OPAMP CIRCUITS IN INSTRUMENTATION
Current-to-Voltage Converter: At the receiving end of the process-control signal transmission system, we often need to convert the current back into a voltage. This can be done most easily with the circuit shown in Figure . This circuit provides an output voltage given by

## Slide 17: Ultrasonic Sensors
Ultrasound waves are pressure waves, just like sound waves, but their frequencies are higher (ultra) than the audible frequencies.
Ultrasonic sensors are used in many applications, including medical imaging, ranging systems for cameras with autofocusing capability, level sensing, and speed sensing. In medical applications, ultrasound probes of frequencies 40 kHz, 75 kHz, 7.5 MHz, and 10 MHz are commonly used.
In distance (range, proximity, displacement) measurement using ultrasound, a burst of ultrasound is projected at the target object, and the time taken for the echo to be received is clocked. A signal processor
computes the position of the target object, possibly compensating for environmental conditions.
The applicable relation is

## Slide 18
where
t is the time of flight of the ultrasound pulse (from generator to receiver) x is the distance between the ultrasound generator/receiver and the target object
c is the speed of sound in the medium (typically, air

## Slide 19
Sensors
Sensor is an element which produces a signal relating to the quantity being
measured.
An input device which provides an output (signal) with respect to a specific physical quantity.
A device that converts signals from one energy domain to electrical domain.

## Slide 20: Sensors

## Slide 21: Classification of Sensors
The sensors are classified into the following criteria:
Primary Input quantity (Measurand)
Transduction principles (Using physical and chemical effects)
Material and Technology
Property
Application

## Slide 22: Classification of Sensors
Active
Sensor: Active Sensors are those which require an external excitation
signal or a power signal. E.g.: LiDAR (Light detection and ranging), photoconductive cell.
Passive Sensor: Do not require any external power signal and directly
generates output response. E.g.:
Radiometers, film
photography
Based on the means of detection
Some of the means of detection are Electric, Biological, Chemical, Radioactive
etc.

## Slide 23: Classification of Sensors
Sensors that are commonly used in various applications.
All these sensors are used for measuring one of the physical properties like Temperature, Resistance, Capacitance, Conduction, Heat Transfer etc.
Temperature Sensor
Proximity Sensor
Accelerometer
IR Sensor
Pressure Sensor
Light Sensor
Ultrasonic Sensor
Smoke, Gas and Alcohol Sensor
Touch Sensor
Color Sensor
Humidity Sensor
Tilt Sensor
Flow and Level Sensor

## Slide 24: Classification of Sensors
Based on the conversion phenomenon i.e. the input and the output.
Some of the conversion phenomena are Photoelectric, Thermoelectric,
Electrochemical, Electromagnetic, Thermo-optic, etc.
Analogue sensors: Produce an analog output.
Digital Sensors: Work with discrete or digital data.

## Slide 25: Transducer / Gauges / Signal Generators / Pickups
A device that converts variations in a physical quantity, such as pressure or brightness, into an electrical signal, or vice versa.
A transducer is an electronic device that converts energy from one form to
another.
E.g. microphones, loudspeakers, thermometers, position and pressure sensors,
and antenna
Transducer
Physical Qty.
Excitation
Electrical Output

## Slide 26
Difference between Sensor and Transducers
Sensors – the term sensor is used for an element which generates a signal which is proportional to the quantity being measured.
Transducer – these are elements
subjected to
experience a
physical
related
when change change.

## Slide 27: Difference between Sensor and Transducers
Basis For Comparison | Sensor | Transducer
Definition | Senses the physical changes occurs in the surrounding and converting it into a readable quantity. | The transducer is a device which, when actuates transforms the energy from one form to another.
Components | Sensor itself | Sensor and signal conditioning
Function | Detects the changes and induces the corresponding electrical signals. | Conversion of one form of energy into another.
Examples | Proximity sensor, Magnetic sensor, Accelerometer sensor, Light sensor, Barometer, Gyroscope etc. | Thermistor, Potentiometer, Thermocouple, etc.

## Slide 50
Sensors for Electromechanical Applications
Motion Transducers
By motion, we particularly mean one or more of the following four kinematic variables:
Displacement (including position, distance, proximity, size, and gauge)
Velocity (rate of change of displacement)
Acceleration (rate of change of velocity)
Jerk (rate of change of acceleration)

## Slide 51
Motion Transducer Selection
In selecting a motion transducer, we need to consider several factors.
Several preliminary considerations
are as follows:
Kinetic nature of the measurand (position, proximity, displacement,
speed, acceleration, etc.)
Rectilinear (commonly termed linear) or rotatory (commonly termed
rotary) motion
Contact or noncontact type
Measurement range
Required accuracy
Required frequency range of operation (time constant, bandwidth)
Size
Cost
Operating environment (e.g., magnetic fields, temperature, pressure, humidity, vibration, shock)
Life expectancy

## Slide 52: Force Sensors for Motion Measurement
An inertia element (to convert acceleration into force, in proportion)
A damping element (to convert velocity into force, in proportion)
A spring element (to convert displacement into force, in proportion)

## Slide 54: Potentiometer

## Slide 55
Linear-Variable Differential Transformer/Transducer

## Slide 56
Linear-Variable Differential Transformer/Transducer

## Slide 59
Now suppose that the core, length L, is moved through a
distance x from the null position

## Slide 61
Signal Conditioning for LVDT

## Slide 62
Signal Conditioning for LVDT

## Slide 63
Signal Conditioning for LVDT

## Slide 64
Advantages of the LVDT include the following:
It is essentially a noncontacting device with no frictional resistance. Near-
ideal electromechanical
energy conversion and lightweight core will result in very small resistive forces.
Hysteresis (both
magnetic hysteresis and mechanical backlash) is negligible.
It has low output impedance, typically in the order of 100 Ω. (Signal
amplification is usually not
needed beyond what is provided by the conditioning circuit.)
It provides directional measurements (positive/negative).
It is available in miniature sizes as well (e.g., length of 1 or 2 mm,
displacement measurements of
a fraction of a millimeter, and maximum travel or stroke of 1 mm)
It has a simple and robust construction (inexpensive and durable)
It has fine resolutions (theoretically, infinitesimal resolution; practically, much better than a coil
potentiometer).

## Slide 65: Mutual-Induction Proximity Sensor
Proximity sensors are used in a wide variety of applications pertaining to noncontacting displacement sensing and dimensional gaging. Some typical applications are
Measurement and control of the gap between a robotic welding torch head and
the work surface
Gaging the thickness of metal plates in manufacturing operations (e.g., rolling
and forming)
Detecting surface irregularities in machined parts
Measurement of angular speed, by counting the number of rotations per unit time
Measurement of vibration in rotating machinery and structures (for machine health monitoring
and control, etc.)
Detection of liquid level (e.g., in the filling, bottling, and chemical process
industries)
Monitoring of bearing assembly processes

## Slide 66
Mutual-Induction Proximity Sensor

## Slide 67
capacitive sensors
(a) Capacitive displacement sensor

## Slide 68
capacitive sensors
(b) capacitive rotation
sensor

## Slide 70
capacitive sensors
(c) capacitive liquid level sensor.

## Slide 71
liquid level (y) is based on the
variation of the dielectric constant (k) of the capacitor, while A and x are kept constant in Equation below Since the voltage in the air segment (a) and the liquid segment (l) of the capacitor is the same while the charges are additive, the capacitances are additive:

## Slide 72
Hence, we can express the liquid level as
where
x is the plate gap
h is the plate height
b is the plate width
ka is the permittivity of air
kl is the permittivity of the liquid

## Slide 73
Applications of Capacitive Sensors
Motion sensing (e.g., wafer positioning in semiconductor (SC) industry, disc drive control,machine-tool control)
Gauging and metrology (e.g., thickness of plates, gauging manufactured parts for
quality control)
Object detection (e.g., counting parts in production lines, detecting cap placement in bottling plants, touch button switches of elevators, etc.)
Liquid level sensing in (e.g., in process plants)
Material testing (e.g., surface properties of objects, detecting water in fuels)
Environmental sensing (e.g., moisture, soil)

## Slide 74
Piezoelectric Sensors
Piezoelectric effect: The piezoelectric effect is caused by the charge polarization in an anisotropic material (having nonsymmetric molecular structure), as a result of an applied strain. Specifically, a charge (or electric field) is released when the material is strained. This is a reversible effect.
In particular, when an electric field is applied to the material, it changes the ionic polarization, and the material sheds the strain (i.e., the original strain is removed and the material regains its original shape).
Natural piezoelectric materials are by and large crystalline, whereas synthetic piezoelectric materials tend to be ceramics.